## Slide 1: Unit 03.03.03 CS 5220: COMPUTER COMMUNICATIONS
Link State Routing, ATM Networks
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: Reaction to Failure
In distance vector routing, if a link fails
    Neighboring routers exchange routing tables that may use failed links
In link-state routing, if a link fails,
  Router sets link distance to infinity & floods the network with an update packet
  All routers immediately update their link database & recalculate their shortest paths
  Recovery very quick

## Slide 3: Why is Link State Better?
Fast, loopless convergence
Support for precise metrics, and multiple metrics if necessary (throughput, delay, cost, reliability)
Support for multiple paths to a destination
  algorithm can be modified to find best two paths

## Slide 4: Problem of Link State Routing
But watch out for old update messages
  Add time stamp or sequence # to each update message
  Check whether each received update message is new
  If new, add it to database and broadcast
  If older, send update message on arriving link

## Slide 5: Source Routing vs. H-by-H
Source host selects path to be followed by a packet
  Strict: sequence of nodes in path inserted into header
  Loose: subsequence of nodes in path specified
Intermediate switches read next-hop address and remove address
  Or maintained for the reverse path
Source routing allows the host to control the paths that its information traverses in the network
Potentially the means for customers to select what service providers they use

## Slide 6: Example
1
2
3
4
5
6
A
B
Source host
Destination host
1,3,6,B
3,6,B
6,B
B

## Slide 7: Asynchronous Tranfer Mode (ATM)
Packet multiplexing and switching
  Fixed-length packets: “cells”
  Connection-oriented
  Rich Quality of Service support
Conceived as end-to-end
  Supporting wide range of services
    Real time voice and video
    Circuit emulation for digital transport
    Data traffic with bandwidth guarantees

## Slide 8: TDM vs. Packet Multiplexing
 | Variable bit rate | Delay | Burst traffic | Processing
TDM | Multirate only | Low, fixed | Inefficient | Minimal, very high speed
Packet | Easily handled | Variable | Efficient | Header & packet processing required
*In mid-1980s, packet processing mainly in software and hence slow; By late 1990s, very high speed packet processing possible

## Slide 9: ATM: Attributes of TDM & Packet Switching
MUX
Wasted bandwidth
ATM
TDM
3 2 1 4 3 2 1 4 3 2 1
4 3 1 3 2 2 1
Voice
Data packets
Images
1
2
3
4
Packet structure gives flexibility & efficiency
Fixed packet length simplifies implementation and makes high speed
Packet Header

## Slide 10: ATM Virtual Connections
Virtual connections setup across network
Connections identified by locally-defined tags
ATM Header contains virtual connection information:
  8-bit Virtual Path Identifier
  16-bit Virtual Channel Identifier
Powerful traffic grooming capabilities
  Multiple VCs can be bundled within a VP
Physical link
Virtual paths
Virtual channels

## Slide 11: MPLS & ATM
ATM initially touted as more scalable than packet switching
Advances in optical transmission proved ATM to be the less scalable: @ 10 Gbps
  Segmentation & reassembly of messages & streams into 48-byte cell payloads difficult & inefficient
  Header must be processed every 53 bytes vs. 500 bytes on average for packets
MPLS (multiprotocol label switching) uses tags to transfer packets across virtual circuits in Internet
  Adopts label switching paradigm, but variable-length packets by packet-over-SONET encapsulation