## Slide 1: Unit 03.03.04 CS 5220: COMPUTER COMMUNICATIONS
RIP and OSPF
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: Routing Information Protocol (RIP)
RIP based on routed, distributed in BSD UNIX
Uses the distance-vector algorithm
Runs on top of UDP, port number 520
Metric: number of hops
Max limited to 15
  suitable for small networks (local area environments)
  value of 16 is reserved to represent infinity
  small number limits the count-to-infinity problem

## Slide 3: RIP Operation
Router sends update message to neighbors every 30 sec
A router expects to receive an update message from each of its neighbors within 180 seconds in the worst case
If router does not receive update message from neighbor X within this limit, it assumes the link to X has failed and sets the corresponding minimum cost to 16 (infinity)
Uses split horizon with poisoned reverse
Convergence speeded up by triggered updates
  neighbors notified immediately of changes in distance vector table

## Slide 4: Deficiencies in RIP Protocol
Limited Metric Use
Slow Convergence

## Slide 5: Open Shortest Path First (OSPF)
Fixes some of the deficiencies in RIP
Enables each router to learn complete network topology
Each router monitors the link state to each neighbor and floods the link-state information to other routers
Each router builds an identical link-state database
Allows router to build shortest path tree with router as root
OSPF typically converges faster than RIP when there is a failure in the network

## Slide 6: OSPF Network
To improve scalability, an autonomous system (AS) may be partitioned into two-level areas
  Area defined by 32-bit area ID
  Routers in area only knows complete topology inside area & limits the flooding of link-state information to area
  Area border routers summarize info from other areas
Each area must connect to backbone area (0.0.0.0)
Internal router has all links to nets within the same area
Area border router has links to more than one area
backbone router has links connected to the backbone
Autonomous system boundary (ASB) router has links to another autonomous system

## Slide 7: OSPF Areas
ASB: 4
Area border router : 3, 6, and 8
Internal router: 1,2,7
Backbone router: 3,4,5,6,8
R = router N = network
Area 0.0.0.1
Area 0.0.0.2
Area 0.0.0.3
R1
R2
R4
R5
R7
N1
N2
N3
N4
N5
N6
N7
To another AS
Area 0.0.0.0
R8
R3
R6