## Slide 1: Unit 03.04.01 CS 5220: COMPUTER COMMUNICATIONS
Packet level – Scheduling and QoS
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: Time Scales & Granularities
Packet Level
  Queueing & scheduling at multiplexing points
  Determines relative performance offered to packets over a short time scale (microseconds)
Flow Level
  Management of traffic flows & resource allocation to ensure delivery of QoS (milliseconds to seconds)
  Matching traffic flows to resources available; congestion control
Flow-Aggregate Level
  Routing of aggregate traffic flows across the network for efficient utilization of resources & meeting of service levels
  “Traffic Engineering”, at scale of minutes to days

## Slide 3: End-to-End QoS
1
2
N
N – 1
Packet buffer
…
A packet traversing network encounters delay and possible loss at various multiplexing points
End-to-end performance is accumulation of per-hop performances
Packet loss occurs when no more buffer available for a packet

## Slide 4: Scheduling & QoS
End-to-End QoS & Resource Control
  Buffer & bandwidth control → Performance
  Admission control to regulate traffic level
Scheduling Concepts
  fairness/isolation, priority, aggregation,
Fair Queueing & Variations
  FQ/WFQ, PGPS
Guaranteed Service
  FQ/WFQ, Rate-control
Packet Dropping

## Slide 5: FIFO Queueing
All packet flows share the same buffer
Transmission Discipline: First-In, First-Out
Buffering Discipline: Discard arriving packets if buffer is full (Alternative: random discard; pushout head-of-line, etc.)
Delay and loss depends on inter-arrival and packet lengths
Packet buffer
Transmission
link
Arriving
packets
Packet discard
when full

## Slide 6: FIFO Queueing
Cannot provide differential QoS to packet flows
  Different packet flows interact strongly
Statistical delay guarantees via load control
  Restrict number of flows allowed (admission control)
  Difficult to determine performance delivered
Finite buffer determines a maximum possible delay
Buffer size determines loss probability
  But depends on arrival & packet length statistics

## Slide 7: FIFO w/o and w/ Discard Priority
Packet buffer
Transmission
link
Arriving
packets
Packet discard
when full
Packet buffer
Transmission
link
Arriving
packets
Class 1
discard
when full
Class 2 discard
when threshold
exceeded
(a)
(b)
FIFO queueing
FIFO queueing
with discard priority

## Slide 8: HOL Priority Queueing
High priority queue serviced until empty
High priority queue has lower waiting time
Buffers can be dimensioned for different loss probabilities
Transmission
link
Packet discard
when full
High-priority
packets
Low-priority
packets
Packet discard
when full
When
high-priority
queue empty

## Slide 9: Summary: HOL Priority Features
Provides differential QoS
High-priority classes can hog all of the bandwidth & starve lower priority classes
Need to provide some isolation between classes
Delay
Per-class loads
(Note: Need labeling)