## Slide 1: Unit 03.04.02 CS 5220: COMPUTER COMMUNICATIONS
Packet Level: Fair Queuing and RED
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: Fair Queuing
Attempts to provide isolated and equitable access transmission bandwidth (like Processor Sharing)
Each user flows has its own logical buffer
Idealized system assumes fluid flow from queues
Weighted fair queueing (WFQ) further addresses different users with different priorities/weights

## Slide 3: Fair Queuing – Fluid
Each flow has its own logical queue: prevents hogging; allows differential loss probabilities
C bits/sec allocated equally among non-empty queues
  transmission rate = C / n(t), where n(t)=# non-empty queues
C bits/second
Transmission
link
Packet flow 1
Packet flow 2
Packet flow n
Approximated bit-level
round robin service
…
…

## Slide 4: Fair Queuing - Approximation
Per-bit round-robin: decomposing the resulting bit stream into the component networks would be costly
In ATM, fair queueing can be approximated easier
In packet networks, implementation requires approximation: simulate fluid system; sort packets according to completion time in ideal system

## Slide 5: Example
(a) A router with five packets queued for line O.
(b) Finishing times for the five packets.
FIFO (per-packet) -> Fair queueing (per-bit)

## Slide 6: Buffer Management
Drop strategy: Which packet to drop when buffers full
Fairness: protect behaving sources from misbehaving ones
Aggregation:
  Per-flow buffers protect flows from misbehaving flows
  Full aggregation provides no protection
  Aggregation into classes provides intermediate protection
Drop priorities:
  Drop packets from buffer according to priorities
  Maximizes network utilization & application QoS
  Examples: layered video, policing at network edge
Controlling sources at the edge

## Slide 7: Random Early Detection (RED)
Random early detection (RED):
Early drop: discard packets before buffers are full; drop packets if short-term average of queue exceeds threshold
Packet drop probability increases linearly with queue length
Random drop causes some sources to reduce rate before others, causing gradual reduction in aggregate input rate
Packets produced by TCP will reduce input rate in response to network congestion
Improves performance of cooperating TCP sources
Increases loss probability of misbehaving sources

## Slide 8: Packet Drop Profile in RED
Average queue length
Probability of packet drop
1
0
minth
maxth
full
Algorithm:
Maintain running average of queue length
If Qavg < minthreshold, do nothing
If Qavg > maxthreshold, drop packet
If in between, drop packet according to probability
Flows that send more packets are more likely to have packets dropped