## Slide 1: Unit 03.04.04 CS 5220: COMPUTER COMMUNICATIONS
Traffic Shaping by Token Bucket
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2
Flow-level Traffic Shaping
Traffic shaping refers to the process of altering a traffic flow to ensure conformance
A traffic shaping device is often located at the node just before traffic flow leaves network
A traffic policing device is usually located at the node that receives the traffic flow from a network

## Slide 3: Leaky Bucket Traffic Shaper
Incoming traffic
Shaped traffic
Size N
Packet
Server
Buffer incoming packets
Play out periodically to conform to parameters
Surges in arrivals are buffered & smoothed out
Possible packet loss due to buffer overflow
Restrctive, not allowing any variable-rate outgoing traffic

## Slide 4: Token Bucket Traffic Shaper
Incoming traffic
Shaped traffic
Size N
Size K
Tokens arrive
periodically
Server
Packet
Token
Token rate regulates transfer of packets
If sufficient tokens available, packets enter network without delay
K determines how much burstiness allowed into the network
An incoming packet must have sufficient tokens before admission into the network

## Slide 5: Token Bucket Shaping Effect (full)
The token bucket constrains the traffic from a source to be limited to b + r t bits in an interval of length t
b bytes instantly
t
r bytes/second
b + r t
Q2: When a token bucket is the same as a leaky bucket?
Q1: what are two main differences of a leaky bucket and a token bucket?
Allow saving for burst spending; packet discarding or not.
b = 0; but still different indeed: packet discarding or not

## Slide 6: Token Bucket Shaping Effect (empty)
Behavior of the token bucket shaper is similar to that of the leady bucket shaper
If the bucket size is reduced to zero, they are identical

## Slide 7: Closed-Loop Flow Control
Congestion control
  Feedback information to regulate flow from sources into network
  Based on buffer length, link utilization, etc.
  Examples: TCP at transport layer; congestion control at ATM level
End-to-end vs. Hop-by-hop
  Delay in effecting control
Implicit vs. Explicit Feedback
  Source deduces congestion from observed behavior
  Routers/switches generate messages alerting to congestion

## Slide 8: E2E vs. H2H Congestion Control
Source
Destination
Feedback information
Packet flow
Source
Destination
(a)
(b)
TCP vs. ATM

## Slide 9: Congestion Warning
The Warning Bit in ACKs
Choke packets to the source
A time-out due to missing acknowledgement

## Slide 10: Aggregate Level - Traffic Engineering
Management exerted at flow aggregate level
Distribution of flows in network to achieve efficient utilization of resources (bandwidth)
Must take into account aggregate demand from all flows
“Traffic Engineering”, at scale of minutes to days