## Slide 1: Unit 03.01.02 CS 5220: COMPUTER COMMUNICATIONS
Network Layer Services and Topology
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: Network Layer
Network Layer: the most complex layer
  Requires the coordinated actions of multiple, geographically distributed network elements (switches & routers)
  Must be able to deal with very large scales
    Billions of users (people & communicating devices)
  Biggest Challenges
    Addressing: where should information be directed to?
    Routing: what path should be used to get information there?

## Slide 3: Packet Switching
t0
t1
Network
Transfer of information as payload in data packets
Packets undergo random delays & possible loss
Different applications impose differing requirements on the transfer of information

## Slide 4
End system
β
Physical
layer
Data link
layer
Physical
layer
Data link
layer
End system
α
Network
layer
Network
layer
Physical
layer
Data link
layer
Network
layer
Physical
layer
Data link
layer
Network
layer
Transport
layer
Transport
layer
Messages
Messages
Segments
Network
service
Network
service
Network Service
Network layer can offer a variety of services to transport layer

## Slide 5: Network Service vs. Operation
Network Service
Connectionless
  Datagram Transfer
Connection-Oriented
  Reliable and possibly constant bit rate transfer
Internal Network Operation
Connectionless
  IP
Connection-Oriented
  ATM
Various combinations are possible
Connection-oriented service over Connectionless operation
Connectionless service over Connection-Oriented operation
Context & requirements determine what makes sense

## Slide 6: Complexity at the Edge or in the Core?
1
1
3
3
2
1
2
2
3
2
1
1
2
2
1
2
1
Medium
A
B
3
2
1
1
2
2
1
C
2
1
2
1
2
1
4
1
2
3
4
End system α
End system β
Network
1
2
Physical layer entity
Data link layer entity
3
Network layer entity
3
Network layer entity
Transport layer entity
4

## Slide 7: The End-to-End Argument for System Design
An end-to-end function is best implemented at a higher level than at a lower level
  End-to-end service requires all intermediate components to work properly
  Higher-level better positioned to ensure correct operation
Example: stream transfer service
  Establishing an explicit connection for each stream across network requires all network elements (NEs) to be aware of connection; All NEs have to be involved in re-establishment of connections in case of network fault
  In connectionless network operation, NEs do not deal with each explicit connection and are much simpler in design

## Slide 8: Network Layer Functions
Essentials
Routing: mechanisms for determining the set of best paths for routing packets that requires the collaboration of network elements
Forwarding: transfer of packets from inputs to outputs
Priority & Scheduling: determining order of packet transmission in each network element
Optional: congestion control, segmentation & reassembly, security

## Slide 9: End-to-End Packet Network Topology
In Packet networks,
Individual packet streams are highly bursty
  Statistical multiplexing is used to concentrate streams
User demand can undergo dramatic change
  Peer-to-peer applications stimulated huge growth in traffic volumes
Internet structure highly decentralized
  Paths traversed by packets can go through many networks controlled by different organizations
  No single entity responsible for end-to-end service

## Slide 10: Access Multiplexing
Access
MUX
To
packet
network
Packet traffic from users multiplexed at access to network into aggregated streams
DSL traffic multiplexed at DSL Access Mux
Cable modem traffic multiplexed at Cable Modem Termination System

## Slide 11: Oversubscription
Access Multiplexer
  N subscribers connected @ c bps to mux
  Each subscriber active r/c of time
  Mux has C = mc bps to network
  Oversubscription ratio: N/m
  Find m so that at most 1% overflow probability
• • •
Nr
Nc
r
r
r
mc
• • •

## Slide 12: Oversubscription Ratio
Feasible oversubscription rate increases with size
N | r/c | m | N/m | 
10 | 0.01 | 1 | 10 | 10 extremely lightly loaded users
10 | 0.05 | 3 | 3.3 | 10 very lightly loaded user
10 | 0.1 | 4 | 2.5 | 10 lightly loaded users
20 | 0.1 | 6 | 3.3 | 20 lightly loaded users
40 | 0.1 | 9 | 4.4 | 40 lightly loaded users
100 | 0.1 | 18 | 5.5 | 100 lightly loaded users
• • •
Nr
Nc
r
r
r
mc
• • •

## Slide 13: Home LANs
Home Router
  LAN Access using Ethernet or WiFi (IEEE 802.11)
  Private IP addresses in Home (192.168.0.x) using Network Address Translation (NAT)
  Single global IP address from ISP issued using Dynamic Host Configuration Protocol (DHCP)
Home
Router
To
packet
network
WiFi
Ethernet

## Slide 14: LAN Concentration
LAN Hubs and switches in the access network also aggregate packet streams that flows into switches and routers
     
     
Switch
/ Router

## Slide 15: Campus Network
R
R
R
R
S
S
S
s
s
s
s
s
s
s
s
s
s
R
s
R
Backbone
To Internet or wide area network
Organization Servers
Departmental Server
Gateway
Only outgoing packets leave LAN through router
High-speed campus backbone net connects dept routers
Servers have redundant connectivity to backbone

## Slide 16: Summary:
End-to-end argument significantly affect networking system design, for performance and scalability
Oversubscription is a common technique with multiplexing for efficiency