## Slide 1: Unit 03.01.03 CS 5220: COMPUTER COMMUNICATIONS
Packet Switching - Datagrams
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: The Switching Function
Dynamic interconnection of inputs to outputs
Enables dynamic sharing of transmission resource
Two fundamental approaches:
  Connectionless
  Connection-Oriented
Backbone Network
Access Network
Switch

## Slide 3: Packet Switching Network
Packet
switch
Network
Transmission
line
User
Packet switching network
Transfers packets between users
Transmission lines + packet switches (routers)
Origin in message switching
Two modes of operation:
Connectionless
Virtual Circuit
Notes: 7-9
The text boxes are callouts or labels.

## Slide 4: Message Switching
Message switching invented for telegraphy
Entire messages multiplexed onto shared lines, stored & forward
Headers for source & destination addresses
Routing at message switches
Connectionless
Switches
Message
Destination
Source
Message
Message
Message
Transmission delay vs. propagation delay
Transmit a 1000B from LA to DC via a 1Gbps network, signal speed 200Km/sec.

## Slide 5: Message Switching Delay
t
t
t
t
Delay
Source
Destination
T

Minimum delay = 3 + 3T
Switch 1
Switch 2
Additional queueing delays possible at each link

## Slide 6: Long Messages vs. Packets
Approach 1: send 1 Mbit message
Probability message arrives correctly
On average it takes about 3 transmissions/hop
Total # bits transmitted ≈ 6 Mbits
1 Mbit
message
source
dest
BER=p=10-6
BER=10-6
How many bits need to be transmitted to deliver message?
Approach 2: send 10 100-kbit packets
Probability packet arrives correctly
On average it takes about 1.1 transmissions/hop
Total # bits transmitted ≈ 2.2 Mbits
Pc = (1 – 10-6)10^6 ≈ e -10^6 10^-6 = e-1 ≈ 1/3
Pc = (1 – 10-6)10^5 ≈ e -10^5 10^-6 = e-1/10 ≈ 0.9

## Slide 7: Packet Switching - Datagram
Messages broken into smaller units (packets)
Source & destination addresses in packet header
Connectionless, packets routed independently (datagram)
Packet may be out of order
Pipelining of packets across network can reduce delay, increase throughput
Lower delay than message switching, suitable for interactive traffic
Packet 2
Packet 1
Packet 1
Packet 2
Packet 2

## Slide 8: Packet Switching Delay
t
t
t
t
Delay
3
1
2
3
1
2
3
2
1
Minimum Delay = 3τ + 5(T/3) (assumed single path, no queueing delay)
Packet pipelining enables message to arrive sooner
Assume three packets corresponding to one message
1/3T
Switch 1
Switch 2
Source
Destination

## Slide 9: Delay for k-Packet Message over L Hops
t
t
t
t
3
1
2
3
1
2
3
2
1
3 + 2(T/3) first bit received
3 + 3(T/3) first bit released
3 + 5 (T/3) last bit released
L + (L-1)P first bit received
L + LP first bit released
L + LP + (k-1)P last bit released
where T = k P
3 hops
L hops
Source
Destination
Switch 1
Switch 2


## Slide 10: Summary:
Long message switching suffers long delay and is more vulnerable to errors.
Packet pipelining reduce delay and improve throughput.