## Slide 1: Unit 03.02.01 CS 5220: COMPUTER COMMUNICATIONS
Packet Switching – Virtual Circuits
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: Packet Switching – Virtual Circuit
Call set-up phase sets ups pointers in fixed path along networks
All packets for a connection follow the same path
Abbreviated header identifies connection on each link
Variable bit rates possible, negotiated during call set-up
Physical-layer circuit vs Network-layer virtual circuit
Virtual circuit
Packet
Packet
Packet
Packet

## Slide 3: Connection Setup
SW 1
SW 2
SW n
Connect request
Connect request
Connect request
Connect confirm
Connect confirm
Connect confirm
…
Signaling messages propagate as route is selected
Signaling messages identify connection and setup tables in switches
Typically a connection is identified by a local tag, Virtual Circuit Identifier (VCI)
Each switch only needs to know how to relate an incoming tag in one input to an outgoing tag in the corresponding output
Once tables are setup, packets can flow along path

## Slide 4: Virtual Circuit Forwarding Tables
Input
VCI
Output
port
Output
VCI
15
15
58
13
13
7
27
12
44
23
16
34
Each input port of packet switch has a forwarding table
Lookup entry for per-link/port VCI of incoming packet
Determine output port (next hop) and insert VCI for next link
Very high speeds are possible (HW-based)
Table can also include priority or other information about how packet should be treated

## Slide 5: Routing in Virtual Circuit Subnet
Label switching

## Slide 6: Virtual Circuit w/ Connection Setup Delay
t
t
t
t
3
1
2
3
1
2
3
2
1
Release
Connect request
CR
CR
Connect confirm
CC
CC
Connection setup delay is incurred before any packet can be transferred
Delay is acceptable for sustained transfer of large number of packets
This delay may be unacceptably high if only a few packets are being transferred

## Slide 7: Example: ATM Networks
All information mapped into short fixed-length packets called cells
Connections set up across network
  Virtual circuits established across networks
  Tables setup at ATM switches
Several types of network services offered
  Constant bit rate connections
  Variable bit rate connections

## Slide 8: Cut-Through Switching
3
1
2
3
1
2
3
2
1
Minimum delay = 3 + T
t
t
t
t
Source
Destination
Switch 1
Switch 2
Some networks perform error checking on header only, so packets can be forwarded as soon as header is received & processed
Delays reduced further with cut-through switching

## Slide 9: Message vs. Packet Minimum Delay
Message switching:
  L t + L T = L t + (L – 1) T + T
Packet switching with store-and-forward
  L t + L P + (k – 1) P = L t + (L – 1) P + T
Cut-Through Packet switching (Immediate forwarding after header) = L t + T
  Above measurements neglect header processing delays

## Slide 10
5-4