## Slide 1: Unit 03.02.02 CS 5220: COMPUTER COMMUNICATIONS
Routing in Packet Networks
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: Routing in Packet Networks
1
2
3
4
5
6
Node
(switch or router)
Three possible (loopfree) routes from 1 to 6:
  1-3-6, 1-4-5-6, 1-2-5-6
Which is “best”?
  Min delay? Min hop? Max bandwidth? Min cost?

## Slide 3: Routing Algorithm Requirements
Responsiveness to changes
  Topology or bandwidth changes, congestion
  Rapid convergence of routers to consistent set of routes
  Freedom from persistent loops
Optimality
  Resource utilization, path length
Robustness
  Continues working under high load, congestion, faults, equipment failures, incorrect implementations
Simplicity
  Efficient software implementation, reasonable processing load

## Slide 4: Creating the Routing Tables
Need information on state of links
  Link up/down; congested; delay or other metrics
Need to distribute link state info using a routing protocol
  What information is exchanged? How often?
  Exchange with neighbors; Broadcast or flood
Need to compute routes based on information
  Single metric; multiple metrics
  Single route; alternate routes

## Slide 5: Routing Tables in Datagram Networks
Destination
address
Output
port
1345
12
2458
7
0785
6
12
1566
Route determined by table lookup
Routing decision involves finding next hop in route to given destination
Routing table has an entry for each destination specifying output port that leads to next hop
Size of table becomes impractical for very large number of destinations

## Slide 6: Example: Internet Routing
Internet protocol uses datagram packet switching across networks
  Networks are treated as data links
Hosts have two-part IP address:
  Network address + Host address
Routers do table lookup on network address
  This reduces size of routing table
In addition, network addresses are assigned so that they can also be aggregated

## Slide 7: Routing in Virtual-Circuit Packet Networks
1
2
3
4
5
6
A
B
C
D
1
5
2
3
7
1
8
5
4
2
3
6
5
2
Switch or router
Host
VCI
Route determined during connection setup
Tables in switches implement forwarding that realizes selected route

## Slide 8: Non-Hierarchical Addresses and Routing
0000 0111 1010 1101
0001 0100 1011 1110
0011 0101 1000 1111
0011 0110 1001 1100
R1
1
2
5
4
3
0000 1 0111 1 1010 1 … …
0001 4 0100 4 1011 4 … …
R2
No relationship between addresses & routing proximity
Routing tables require 16 entries each

## Slide 9: Hierarchical Addresses and Routing
0000 0001 0010 0011
0100 0101 0110 0111
1100 1101 1110 1111
1000 1001 1010 1011
R1
R2
1
2
5
4
3
00 1 01 3 10 2 11 3
00 3 01 4 10 3 11 5
Prefix indicates network where host is attached
Routing tables require 4 entries each

## Slide 10: Specialized Routing
Flooding
  Useful in starting up network
  Useful in propagating information to all nodes
Deflection Routing
  Fixed, preset routing procedure
  No route synthesis

## Slide 11: Flooding
Send a packet to all nodes in a network
No routing tables available
Need to broadcast packet to all nodes (e.g. to propagate link state information)
Approach
Send packet on all ports except one where it arrived
Exponential growth in packet transmissions

## Slide 12
1
2
3
4
5
6
Flooding is initiated from Node 1: Hop 1 transmissions

## Slide 13
1
2
3
4
5
6
Flooding is initiated from Node 1: Hop 2 transmissions

## Slide 14
1
2
3
4
5
6
Flooding is initiated from Node 1: Hop 3 transmissions

## Slide 15: Limited Flooding
Time-to-Live field in each packet limits number of hops to certain diameter
Each router adds its ID before flooding; discards repeats
Source puts sequence number in each packet; switches records source address and sequence number and discards repeats

## Slide 16: Deflection Routing
Network nodes forward packets to preferred port
If preferred port busy, deflect packet to another port
Works well with regular topologies
  Manhattan street network
  Rectangular array of nodes
  Nodes designated (i,j)
  Rows alternate as one-way streets
  Columns alternate as one-way avenues
Bufferless operation is possible
  Proposed for optical packet networks
  All-optical buffering currently not viable

## Slide 17
0,0
0,1
0,2
0,3
1,0
1,1
1,2
1,3
2,0
2,1
2,2
2,3
3,0
3,1
3,2
3,3
Tunnel from last column to first column or vice versa
Manhattan Street Network

## Slide 18: Summary:
Routing algorithm optimality depends on the objective function that the network operator tries to optimize
Hierarchical addressing reduces the size of routing table
Flooding is useful when routing tables are unavailable